NHS CFH National SPINE 2087 External Interface Specification: Appendix C: Message Validation Issue 11.6 Draft C 26th November 2008

# Document Control

| Title | 2087 External Interface Specification: Appendix C: Message Validation |
| --- | --- |
| Author | Joe Partridge |
| Doc Ref | 2087 EIS11.6--Part C--Validation.doc |

Note: The document history is held in part one of this document.

# Table of Contents

C	Appendix C	5

C.1	Introduction	5

C.1.1	Overview	5

C.1.2	Changes	5

C.2	Message Validations	6

C.2.1	Multi-Hop End-Party Reliability Message and Multi-Hop No-party Reliability Patterns	6

C.2.1.1	End-Party Reliability	6

C.2.1.2	No-Party Reliability	7

C.2.1.3	LMS Messages	7

C.2.1.4	Non-LMS Messages	8

C.2.1.5	P1R2 and LMS Messages	9

C.2.2	Multi-Hop Intermediary Reliability Message Pattern	9

C.2.3	ebXML Reliable Asynchronous Message Pattern	12

C.2.3.1	P1R2 Batch messages	14

C.2.3.2	P1R2 Non-Batch messages	16

C.2.3.3	P1R1 Non-Batch messages	19

C.2.4	ebXML Unreliable Asynchronous Message Pattern	21

C.2.5	Web Service (P1R1) Message Pattern	25

C.2.6	Web Service (P1R2) Message Pattern	29

C.2.7	Web Service (Non-HL7) Pattern	34

C.2.7.1	QASI Messages	34

C.2.7.2	Get Transmission Parameters Messages	35

C.3	Additional Validation	36

C.3.1	36

# Appendix C

## Introduction

### Overview

This section records the validation rules implemented by the service provider or intermediary where applicable (SPINE) on messages entering SPINE via core message patterns. These include:

- Multi-Hop End-Party Reliability Message AND Multi-Hop No-Party Reliability Patterns

- Multi-Hop Intermediary Reliability Message Pattern

- ebXML Reliable Asynchronous Message Pattern

- ebXML Unreliable Asynchronous Message Pattern

- Web Service (P1R1) Message Pattern

- Web Service (P1R2) Message Pattern

This information is provided to inform service consumers (LSPs & ESPs) as to the level of validation performed by the service provider (SPINE). To accurately and concisely describe validation rules XPath expressions have been maintained. Thus readers are assumed to be familiar with XPath and regular expressions.

### Changes

The following changes have been made to the validations since issue 11.1 –

- Separation of No-Party Reliability and End-Party Reliability specific validation (2.1.1, 2.1.2)

- Addition of two Large Messaging specific validations (2.1.3).

- Addition of ASID checking on P1R2 Forward Express and LMS messages. (C.2.1.5)

## Message Validations

### Multi-Hop End-Party Reliability Message and Multi-Hop No-party Reliability Patterns

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Input protocol | not(string-length(normalize-space(translate(HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| ebXML part | The combination of ebXML service and ebXML action must be supported for the message pattern | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this interaction | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| ebXML part | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| Whole message | All content types of all MIME parts in the message are supported | SOAP Fault |
| ebXML part | /SOAP:Envelope/SOAP:Body/eb:Manifest/@eb:version='2.0' or count(/SOAP:Envelope/SOAP:Body/eb:Manifest) = 0 | SOAP Fault |
| ebXML part | /SOAP:Envelope/SOAP:Header/eb:MessageHeader/@eb:version = '2.0 | SOAP Fault |
| ebXML part | count(/SOAP:Envelope/SOAP:Header/eb:SyncReply)=0 | SOAP Fault |
| ebXML part | The message MUST conform to the ebXML 2.0 schema | SOAP Fault |

#### End-Party Reliability

The validations below apply only to End-Party Reliability messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| ebXML part | count(/SOAP:Envelope/SOAP:Header/eb:AckRequested)=1 | SOAP Fault |
| ebXML part | /SOAP:Envelope/SOAP:Header/eb:AckRequested/@eb:version = '2.0' | SOAP Fault |
| ebXML part | /SOAP:Envelope/SOAP:Header/eb:AckRequested/@eb:signed = 'false' | SOAP Fault |
| ebXML part | /SOAP:Envelope/SOAP:Header/eb:AckRequested/@SOAP:actor = 'urn:oasis:names:tc:ebxml-msg:actor:toPartyMSH' | SOAP Fault |

#### No-Party Reliability

The validation below applies only to No-Party Reliability messages and the ebXML Acknowledgment and MessageError interactions.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| ebXML part | count(/SOAP:Envelope/SOAP:Header/eb:AckRequested)=0 | SOAP Fault |

#### LMS Messages

The validations below apply only to LMS messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| ebXML part | not(/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action[1]/text()=’ CloseSequenceResponse’ or ‘TerminateSequence’) OR string-length(/SOAP:Envelope/SOAP:Header/eb:MessageHeader/nasp:messageHeader/nasp:messageId/text())>0 | SOAP Fault |
| ebXML part | not(/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action[1]/text()=’ CloseSequenceResponse’ or ‘TerminateSequence’) OR string-length(/SOAP:Envelope/SOAP:Header/eb:MessageHeader/nasp:messageHeader/nasp:interactionID/text())>0 | SOAP Fault |
| ebXML part and LDAP | There is one and only one MHS record for the contract in SDS, where – CPA-ID = /soap:Envelope[1]/soap:Header[1]/ eb:MessageHeader[1]/eb:CPAId[1]/ SyncReplyMode = ‘none’ Ack Requested = ‘always’ Duplicate Elimination = ‘always’ Actor = 'urn:oasis:names:tc:ebxml-msg:actor:nextMSH' Party Key = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:To[1]/eb:PartyId[1] Service = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Service Action = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Action Endpoint is of non-zero length | None |

#### Non-LMS Messages

The validation below applies to all messages other than LMS messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| ebXML part and LDAP | There is one and only one entry in SDS for the recipient business service, where – Service = /soap:Envelope[1]/soap:Header[1]/ebxml:MessageHeader[1]/ebxml:Service[1]/text() Recipient party = /soap:Envelope[1]/soap:Header[1]/ebxml:MessageHeader[1]/ebxml:To[1]/ebxml:PartyId[1]/text() AND Associated with this business service record in SDS is one and only one entry for the action of this message, where – Action = /soap:Envelope[1]/soap:Header[1]/ebxml:MessageHeader[1]/ebxml:Action[1]/text() | None |

#### P1R2 and LMS Messages

The validations below apply only to P1R2 (End Party Reliability and No-Party Reliability) and LMS messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| HL7 part, ebXML part and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message originator, where – AS UID for P1R2 messages = (HL7 part)/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension AS UID for LMS messages = (ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/nasp-external:messageHeader/nasp-external:fromASID/text() Accredited Interaction = concat((ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Service/text(), ':', (ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Action/text()) | SOAP Fault |
| HL7 part, ebXML part and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message recipient, where – AS UID for P1R2 messages = (HL7 part)/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension AS UID for LMS messages = (ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/nasp-external:messageHeader/nasp-external:toASID/text() Accredited Interaction = concat((ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Service/text(), ':', (ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Action/text()) | SOAP Fault |

### Multi-Hop Intermediary Reliability Message Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Input protocol | not(string-length(normalize-space(translate(HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| ebXML part | The combination of ebXML service and ebXML action must be supported for the message pattern | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this interaction | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Input protocol | All content types of all MIME parts in the message are supported | SOAP Fault |
| ebXML part | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| ebXML part | The message MUST conform to the ebXML 2.0 schema | SOAP Fault |
| ebXML part and HL7 part | substring-after((ebXML part)/soap:Envelope/soap:Body/eb:Manifest[1]/eb:Reference[1]/@xlink:href,':') = Content-ID header of HL7 part AND string-length(Content-ID header of HL7 part) > 0 | ebXML Error |
| ebXML part | /soap:Envelope/soap:Header/eb:MessageHeader/@eb:version = '2.0' | ebXML Error |
| ebXML part | /soap:Envelope/soap:Body/eb:Manifest/@eb:version = '2.0' | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:SyncReply) = 0 | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:AckRequested) = 1 | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:DuplicateElimination) = 1 | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@eb:version = '2.0' | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@soap:actor = 'urn:oasis:names:tc:ebxml-msg:actor:nextMSH' | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@eb:signed = 'false' | ebXML Error |
| ebXML part | If an ebXML MVI action is present then the combination of ebXML service and ebXML MVI action must be supported for the message pattern. | ebXML Error |
| ebXML part and LDAP | There is one and only one MHS record for the contract in SDS, where – CPA-ID = /soap:Envelope[1]/soap:Header[1]/ eb:MessageHeader[1]/eb:CPAId[1]/ SyncReplyMode = ‘none’ Ack Requested = ‘always’ Duplicate Elimination = ‘always’ Actor = 'urn:oasis:names:tc:ebxml-msg:actor:nextMSH' Party Key = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:To[1]/eb:PartyId[1] Service = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Service Action = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Action Endpoint is of non-zero length | ebXML Error |
| ebXML part | not(/soap:Envelope[1]/soap:Body[1]/eb:Manifest/eb:Reference/nasp:NaspRef/@sseq) OR /soap:Envelope[1]/soap:Body[1]/eb:Manifest/eb:Reference/nasp:NaspRef/@sseq != 1 OR ( /soap:Envelope[1]/soap:Body[1]/eb:Manifest/eb:Reference/nasp:NaspRef/@sseq = 1 AND /soap:Envelope[1]/soap:Body[1]/eb:Manifest/eb:Reference/hl7ebxml:Payload/@style = 'HL7' ) | ebXML Error |
| HL7 part, ebXML part and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message originator, where – AS UID = (HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension Accredited Interaction = concat((ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Service/text(),':',(ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Action/text()) If an MVI tranformation is applied to the message payload, the output interaction ID will be used in place of the input value of eb:Action. | Application Acknowledgement |
| HL7 part, ebXML part and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message recipient, where – AS UID = (HL7 part)/*[1]/hl7:communicationFunctionRcv[1]/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension Accredited Interaction = concat((ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Service/text(),':',(ebXML part)/soap:Envelope/soap:Header/eb:MessageHeader/eb:Action/text()) | Application Acknowledgement |

### ebXML Reliable Asynchronous Message Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Input protocol | not(string-length(normalize-space(translate(HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| ebXML part | The combination of ebXML service and ebXML action must be supported for the message pattern | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this interaction | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Whole message | All content types of all MIME parts in the message are supported | SOAP Fault |
| ebXML part | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| ebXML part | The message MUST conform to the ebXML 2.0 schema | SOAP Fault |
| ebXML part and LDAP | There is one and only one MHS record for the contract in SDS, where – CPA-ID = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:CPAId[1] Party Key = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:To[1]/eb:PartyId[1] Service = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Service Action = /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Action | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:DuplicateElimination) = 1 | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:AckRequested) = 1 | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Header[1]/eb:SyncReply) = 1 | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:SyncReply/@eb:version = '2.0' | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:SyncReply/@soap:actor = 'http://schemas.xmlsoap.org/soap/actor/next' | ebXML Error |
| ebXML part and HL7 part | substring-after((ebXML part)/soap:Envelope[1]/soap:Body[1]/eb:Manifest[1]/eb:Reference[1]/@xlink:href,':') = Content-ID header of HL7 part AND string-length(Content-ID header of HL7 part) > 0 | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/@eb:version = '2.0' | ebXML Error |
| ebXML part | count(/soap:Envelope[1]/soap:Body[1]/eb:Manifest[@eb:version != '2.0'])=0 | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@eb:version = '2.0' | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@eb:signed = 'false' | ebXML Error |
| ebXML part | /soap:Envelope[1]/soap:Header[1]/eb:AckRequested/@soap:actor = 'urn:oasis:names:tc:ebxml-msg:actor:toPartyMSH' | ebXML Error |

#### P1R2 Batch messages

The validations below apply only to P1R2 Batch messages processed by this pattern.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| HL7 part | count(/npfit:*[1]/hl7:id) = 1 AND string-length(normalize-space(/npfit:*[1]/hl7:id/@root))> 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:creationTime) = 1 AND string-length(/npfit:*[1]/hl7:creationTime/@value) > 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:versionCode) = 1 AND string-length(/npfit:*[1]/hl7:versionCode/@code) > 0 | Application Acknowledgement |
| HL7 part and ebXML part | count((HL7 part)/npfit:*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']) = 1 AND (HL7 part)/npfit:*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = (ebXML part)/soap:Envelope[1]/soap:Header[1]/eb:MessageHeader[1]/eb:Action AND (HL7 part)/npfit:*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = local-name((HL7 part)/npfit:*[1]) | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']) = 1 AND string-length(/npfit:*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']/@extension) > 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']) = 1 AND string-length(/npfit:*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']/@extension) > 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/npfit:batchControlActEvent/npfit:batchControlActItem) > 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:manifestItem/hl7:payloadId[normalize-space(@root)='']) = 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/npfit:batchControlActEvent/npfit:batchControlActItem[normalize-space(@messageId)='']) = 0 | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:manifestItem) = /npfit:*[1]/hl7:transmissionQuantity/@value AND count(/npfit:*[1]/npfit:batchControlActEvent/npfit:batchControlActItem) = /npfit:*[1]/hl7:transmissionQuantity/@value | Application Acknowledgement |
| HL7 part | count(/npfit:*[1]/hl7:batchSequenceNo/hl7:value[@root = '2.16.840.1.113883.2.1.3.2.4.18.10']/@extension) = 1 AND string-length(translate(normalize-space(/npfit:*[1]/hl7:batchSequenceNo/hl7:value[@root = '2.16.840.1.113883.2.1.3.2.4.18.10']/@extension),'0123456789','')) = 0 AND string-length(normalize-space(/npfit:*[1]/hl7:batchSequenceNo/hl7:value[@root = '2.16.840.1.113883.2.1.3.2.4.18.10']/@extension)) > 0 | Application Acknowledgement |
| HL7 part | There are no duplicate batch item message IDs in the message | Application Acknowledgement |
| HL7 part | Manifest item interaction IDs are the same as the batched item interaction IDs | Application Acknowledgement |
| HL7 part | not(count(Unique item message IDs)!=/npfit:*[1]/hl7:transmissionQuantity/@value) | Application Acknowledgement |
| HL7 part and LDAP | There is an entry for the originator accredited system in SDS, where the AS ID is given by /*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension This entry must indicate that the system is accredited for all the batched message types, as well as for the interaction given by - concat((ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Service/text(),':',(ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Action/text()) | Application Acknowledgement |

#### P1R2 Non-Batch messages

The validations below apply only to P1R2 non-batch messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| HL7 part | count(/*[1]/hl7:id) = 1 AND string-length(normalize-space(/*[1]/hl7:id/@root))> 0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:creationTime) = 1 AND string-length(/*[1]/hl7:creationTime/@value) > 0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:versionCode) = 1 AND string-length(/*[1]/hl7:versionCode/@code) > 0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent) = 1 | Application Acknowledgement |
| HL7 part and ebXML part | count((HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']) = 1 AND (HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = (ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action[1] AND HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = local-name((HL7 part)/*[1] | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']) = 1 AND string-length(/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']/@extension) > 0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']) = 1 AND string-length(/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']/@extension) > 0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author) = 0 OR ( count(/*[1]/hl7:ControlActEvent[1]/hl7:author) = 1 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.67']) = 1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.67']/@extension)>0 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.65']) = 1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.65']/@extension)>0 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root = '1.2.826.0.1285.0.2.1.104']) = 1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root = '1.2.826.0.1285.0.2.1.104']/@extension)>0 ) | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1)=1 OR count(/*[1]/hl7:ControlActEvent[1]/hl7:author1)=2 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.107'])=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root = '1.2.826.0.1285.0.2.0.107']/@extension)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=0 OR ( count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@root)>0 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@extension)>0 ) | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:*[local-name() = 'query' or local-name() = 'subject']) = 1 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:*[local-name() = 'query' or local-name() = 'subject']/hl7:*) > 0 | Application Acknowledgement |
| ebXML part, HL7 part and LDAP | There is an entry for the originator accredited system in SDS, where the AS ID is given by (HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension This entry must show that the system is accredited for the interaction given by - concat((ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Service/text(),':',(ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Action/text()) | Application Acknowledgement |

#### P1R1 Non-Batch messages

The validations below apply only to P1R1 non-batch messages.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| HL7 part | count(/*[1]/hl7:id)=1 AND string-length(normalize-space(/*[1]/hl7:id/@root))>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:creationTime)=1 AND string-length(/*[1]/hl7:creationTime/@value)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:versionCode)=1 AND string-length(/*[1]/hl7:versionCode/@code)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent) + count(/*[1]/hl7:ControlActProcess) + count(/*[1]/hl7:ControlActRequest) = 1 | Application Acknowledgement |
| HL7 part and ebXML part | count()HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']) = 1 AND (HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = (ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action[1] AND (HL7 part)/*[1]/hl7:interactionId[@root = '2.16.840.1.113883.2.1.3.2.4.12']/@extension = local-name((HL7 part)/*[1]) | Application Acknowledgement |
| HL7 part and ebXML part | count((HL7 part)/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']) = 1 AND string-length((HL7 part)/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']/@extension) > 0 AND (HL7 part)/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']/@extension=(ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:To/eb:PartyId/text() | Application Acknowledgement |
| HL7 part and ebXML part | count((HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']) = 1 AND string-length((HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']/@extension) > 0 AND (HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10']/@extension=(ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:From/eb:PartyId/text() | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent/hl7:subject) + count(/*[1]/hl7:ControlActProcess/hl7:pdsAdvancedTraceQuery) + count(/*[1]/hl7:ControlActRequest/hl7:lRDetailsRequest) = 1 AND count(/*[1]/hl7:ControlActEvent/hl7:subject/hl7:* ¦ /*[1]/hl7:ControlActProcess/hl7:pdsAdvancedTraceQuery/hl7:* ¦ /*[1]/hl7:ControlActRequest/hl7:lRDetailsRequest/hl7:*) > 0 | Application Acknowledgement |

### ebXML Unreliable Asynchronous Message Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Whole message | All content types of all MIME parts in the message are supported | SOAP Fault |
| Input protocol | not(string-length(normalize-space(translate((HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| ebXML part | The combination of ebXML service and ebXML action must be supported for the message pattern | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this interaction | SOAP Fault |
| ebXML part | not(count(/SOAP:Envelope/SOAP:Body/eb:Manifest/eb:Reference) !=1) | ebXML Error |
| ebXML part and HL7 part | not(substring-after(/SOAP:Envelope/SOAP:Body/eb:Manifest/eb:Reference/@xlink:href,':') != (Content ID header of HL7 part)) | ebXML Error |
| ebXML part | /SOAP:Envelope/SOAP:Header/eb:MessageHeader/@eb:version='2.0' OR not(/SOAP:Envelope/SOAP:Header/eb:MessageHeader/@eb:version)) | ebXML Error |
| ebXML part | /SOAP:Envelope/SOAP:Body/eb:Manifest/@eb:version='2.0' OR not(/SOAP:Envelope/SOAP:Body/eb:Manifest/@eb:version) | ebXML Error |
| ebXML part | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| ebXML part | The message MUST conform to the ebXML 2.0 schema | SOAP Fault |
| ebXML part and LDAP | There is one and only one MHS record for the contract in SDS, where – CPA-ID = /SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:CPAId[1] Party Key = /SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:To[1]/eb:PartyId[1] Service = /SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Service Action = /SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action | ebXML Error |
| ebXML part | count(/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:DuplicateElimination)=0 | ebXML Error |
| ebXML part | count(/SOAP:Envelope[1]/SOAP:Header[1]/eb:AckRequested)=0 | ebXML Error |
| HL7 part | count(/*[1]/hl7:id)=1 AND string-length(/*[1]/hl7:id/@root)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:creationTime)=1 AND string-length(/*[1]/hl7:creationTime/@value)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:versionCode)=1 AND string-length(/*[1]/hl7:versionCode/@code)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent)=1 | Application Acknowledgement |
| HL7 part and ebXML part | count((HL7 part)/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'])=1 AND (HL7 part)/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12']/@extension=(ebXML part)/SOAP:Envelope[1]/SOAP:Header[1]/eb:MessageHeader[1]/eb:Action[1] AND (HL7 part)/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12']/@extension=local-name((HL7 part)/*[1]) | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author)=0 OR ( count(/*[1]/hl7:ControlActEvent[1]/hl7:author)=1 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.67'])=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.67']/@extension)>0 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.65'])=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.65']/@extension)>0 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root='1.2.826.0.1285.0.2.1.104'])=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root='1.2.826.0.1285.0.2.1.104']/@extension)>0 ) | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1)=1 OR count(/*[1]/hl7:ControlActEvent[1]/hl7:author1)=2 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=0 OR ( count(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=1 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@root)>0 AND string-length(/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@extension)>0 ) | Application Acknowledgement |
| HL7 part | count(/*[1]/hl7:ControlActEvent[1]/hl7:query)=1 AND count(/*[1]/hl7:ControlActEvent[1]/hl7:query/*)>0 | Application Acknowledgement |
| HL7 part, ebXML part and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message originator, where – AS UID = (HL7 part)/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension Accredited Interaction = concat((ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Service/text(),':',(ebXML part)/SOAP:Envelope/SOAP:Header/eb:MessageHeader/eb:Action/text()) | Application Acknowledgement |

### Web Service (P1R1) Message Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Input protocol | not(string-length(normalize-space(translate((HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this pattern | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Whole message | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Header/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension)=1 AND string-length(SOAP:Envelope/SOAP:Header/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension)>0 AND SOAP:Envelope/SOAP:Header/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension is supported for value of HTTP SOAPAction header | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Header/*[1]/hl7:id/@root[1])=1 AND string-length(SOAP:Envelope/SOAP:Header/*[1]/hl7:id/@root[1])>0 | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)=1 AND string-length(SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)>0 | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)=1 AND string-length(SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)>0 | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension)=1 AND SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension=SOAP:Envelope/SOAP:Header/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension AND SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension=local-name(SOAP:Envelope/SOAP:Body/*[1]) | Application Acknowledgement |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:id[1]/@root)=1 AND SOAP:Envelope/SOAP:Body/*[1]/hl7:id[1]/@root=SOAP:Envelope/SOAP:Header/*[1]/hl7:id/@root[1] | Application Acknowledgement |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:creationTime[1]/@value)=1 AND string-length(SOAP:Envelope/SOAP:Body/*[1]/hl7:creationTime[1]/@value)>0 | Application Acknowledgement |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:versionCode[1]/@code)=1 AND string-length(SOAP:Envelope/SOAP:Body/*[1]/hl7:versionCode[1]/@code)>0 | Application Acknowledgement |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)=1 AND SOAP:Envelope/SOAP:Body/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension=SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension | Application Acknowledgement |
| Whole message | count(SOAP:Envelope/SOAP:Body/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension)=1 AND SOAP:Envelope/SOAP:Body/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension=SOAP:Envelope/SOAP:Header/*[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='2.16.840.1.113883.2.1.3.2.4.10'][1]/@extension | Application Acknowledgement |
| Whole message | not( SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension='QUPA_IN010000UK01' AND not(count(SOAP:Envelope/SOAP:Body/*[1]/hl7:ControlActProcess/hl7:pdsTraceQuery/*)>0) ) | Application Acknowledgement |
| Whole message | not( SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension='QUPA_IN040000UK01' AND not(count(SOAP:Envelope/SOAP:Body/*[1]/hl7:ControlActProcess/hl7:pdsRetrievalQuery/*)>0) ) | Application Acknowledgement |
| Whole message | not( SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension='QUPA_IN060000UK01' AND not(count(SOAP:Envelope/SOAP:Body/*[1]/hl7:ControlActProcess/hl7:pdsConfirmNhsNumberQuery/*)>0) ) | Application Acknowledgement |
| Whole message | not( SOAP:Envelope/SOAP:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'][1]/@extension='QUPC_IN010000UK01' AND not(count(SOAP:Envelope/SOAP:Body/*[1]/hl7:ControlActRequest/hl7:lRConfirmationRequest/*)>0) ) | Application Acknowledgement |

### Web Service (P1R2) Message Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Input protocol | not(string-length(normalize-space(translate((HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this pattern | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Whole message | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/wsa:MessageID)=1 AND string-length(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/wsa:MessageID)=41 | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/wsa:Action)=1 AND SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1] /wsa:Action=(HTTP SOAPAction header) Note that if the HTTP SOAP Action header begins with the string ‘urn:urn:’, this will be amended to ‘urn:’ for the purposes of the validation. | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/wsa:To)=1 AND string-length(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/wsa:To)>0 | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(SOAP-ENV:Envelope[1]/SOAP-ENV:Header[1]/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | SOAP Fault |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:id)=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:id/@root)>0 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:creationTime)=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:creationTime/@value)>0 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:versionCode)=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:versionCode/@code)>0 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent)=1 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12'])=1 AND SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12']/@extension=substring-after(SOAP-ENV:Envelope/SOAP-ENV:Header/wsa:Action,'/') AND SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:interactionId[@root='2.16.840.1.113883.2.1.3.2.4.12']/@extension=local-name(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]) | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:communicationFunctionRcv/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension=SOAP-ENV:Envelope/SOAP-ENV:Header/hl7:communicationFunctionRcv[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:communicationFunctionSnd/hl7:device/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension=SOAP-ENV:Envelope/SOAP-ENV:Header/hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author)=0 OR ( count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author)=1 AND count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.67'])=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.67']/@extension)>0 AND count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.65'])=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:agentPersonSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.65']/@extension)>0 AND count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root='1.2.826.0.1285.0.2.1.104'])=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author/hl7:AgentPersonSDS/hl7:part/hl7:partSDSRole/hl7:id[@root='1.2.826.0.1285.0.2.1.104']/@extension)>0 ) | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1)=1 OR count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1)=2 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.107'])=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[1]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id[@root='1.2.826.0.1285.0.2.0.107']/@extension)>0 | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=0 OR ( count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id)=1 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@root)>0 AND string-length(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:author1[2]/hl7:AgentSystemSDS/hl7:agentSystemSDS/hl7:id/@extension)>0 ) | Application Acknowledgement |
| Whole message | count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:query)=1 AND count(SOAP-ENV:Envelope/SOAP-ENV:Body/*[1]/hl7:ControlActEvent[1]/hl7:query/*)>0 | Application Acknowledgement |
| Message and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message originator, where – AS UID = SOAP-ENV:Envelope/SOAP-ENV:Body/*[1] /hl7:communicationFunctionSnd[1]/hl7:device[1]/hl7:id[@root='1.2.826.0.1285.0.2.0.107'] /@extension Accredited Interaction = translate($request/SOAP:Envelope/SOAP:Header/wsa:Action,'/',':') | SOAP Fault |

### Web Service (Non-HL7) Pattern

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Whole message | The message MUST conform to the SOAP 1.1 schema | SOAP Fault |
| Input protocol | not(string-length(normalize-space(translate((HTTP SOAPAction header),'"',''))) = 0) | SOAP Fault |
| Input protocol | The HTTP SOAPAction header must be supported for this pattern | SOAP Fault |
| Whole message | Number of MIME parts is within allowed range for pattern | SOAP Fault |
| Whole message | Message size is not greater than maximum allowed for pattern | SOAP Fault |
| Message and LDAP | There is one and only one entry in SDS representing the Accredited System that is the message originator, where – AS UID = SOAP:Envelope/SOAP:Header/nasp:messageHeader /nasp:fromASID Accredited Interaction = translate($request/SOAP:Envelope/SOAP:Header/wsa:Action,'/',':') | SOAP Fault |

#### QASI Messages

The validations below apply only to QASI messages processed by this pattern.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Whole message | SOAP:Envelope/SOAP:Header !='' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp:messageHeader/nasp:toASID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp:messageHeader/nasp:fromASID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp:messageHeader/nasp:creationTime != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:MessageID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:Action != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:To != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Body/nasp:searchAccreditedSystemsRequest/nasp:service != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Body/nasp:searchAccreditedSystemsRequest/nasp:interactionID != '' | SOAP Fault |

#### Get Transmission Parameters Messages

The validations below apply only to GetTransmissionParameters messages processed by this pattern.

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| Whole message | SOAP:Envelope/SOAP:Header != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp-external:messageHeader/nasp-external:toASID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp-external:messageHeader/nasp-external:fromASID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/nasp-external:messageHeader/nasp-external:creationTime != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:Action != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:MessageID != '' | SOAP Fault |
| Whole message | SOAP:Envelope/SOAP:Header/wsa:To != '' | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:interactionID)=1 AND SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:interactionID != '' | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:toASID)=1 AND SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:toASID != '' | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:fromASID)=1 AND SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:fromASID != '' | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:messageId)=1 AND SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:messageId != '' | SOAP Fault |
| Whole message | count(SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:messageSize)=1 AND SOAP:Envelope/SOAP:Body/nasp-external:TransmissionParametersRequest/nasp-external:messageSize != '' | SOAP Fault |

## Additional Validation

Note that in addition to the validation described above the following validation:

| Input to validate | Validation | Observable exception |
| --- | --- | --- |
| //@xsi:schemaLocation | Optional. However, if present must be a valid URI. It is recommend to avoid using this attribute if possible. | SOAP Fault |

Will take place on the following patterns:

- Multi-Hop End-Party Reliability Message Pattern

- Multi-Hop Intermediary Reliability Message Pattern

- ebXML Reliable Asynchronous Message Pattern

- ebXML Unreliable Asynchronous Message Pattern

- Web Service Message Patterns

# Footnotes

Effort has been made to include as many known validation rules as possible. However, service consumers should be aware that this document primarily represents explicit validation rules and may not include all implicit validation rules that may occur where these have not be consciously designed and configured.